## Slide 1: Overview of Breadboard #2 for BTNRH
December 2, 2016
WEA

## Slide 2: Overview of Breadboard #2
Teensy 3.6
Power Switch
Built-In Mics
Recharge (USB)

## Slide 3: Getting Started (If the battery isn’t dead)
(1) Plug In Headphones
(2) Turn Down Volume
(3) Turn On System
(5) Listen!
(4) Turn Up Volume

## Slide 4: Powering / Recharging
(1) Plug In USB
(2) Red Means It’s Charging
Green Means It’s Charged.

## Slide 5: Hardware Elements
Processor Board: Teensy 3.6
  Buy. Pinout. Schematic.
Audio Interface: Teensy Audio Board
  Buy. Pinout and Schematic.
Built-In Microphones: Knowles SPW2430
  Buy Breakout. Knowles Product Page.
Bluetooth: RN-42
  Buy Breakout. User Intro.
Battery: Lithium Ion Polymer
  Buy. (choose any size >= 350 mA-hr)

## Slide 6: Elements of BB#2: Audio Sources
System is pre-wired with two small microphones (“Local”)
  Or, you can switch to Aux Input instead (“Jack”)
Aux Input is stereo. Use as line-in.
  Or, it has switchable bias (~2V) to enable electret mics!
Aux Input
Microphone
Switch Mics
to Aux Input
Switchable Bias
For Aux Input
Microphone

## Slide 7: Elements of BB#2: Audio Output
Headphone
Jack
Programmable Knob
(Usually Gain)
Headphone jack is the only output
  Using it as a line-out may cause ground issues. I only use it as a line-out with a battery-powered audio recorder
The blue knob is usually gain (or volume)
  Can be re-programmed to be whatever function you’d like

## Slide 8: Elements of BB#2: Power
Powered from Battery or from USB
Battery recharges while USB is plugged in.
  Red light while charging. Green light when charged.
Power Switch
Battery
Battery Status LEDs
Red=Charging, Green=Done
Power Input
(USB)

## Slide 9: Elements of BB#2: Bluetooth
Has a Bluetooth Classic (not BLE) module
  Is connected to Teensy’s “Serial1” port
  Not really used right now. Will be used in future updates.
Connects to PCs and to Android devices (not iOS)
  Default Pairing Code is “1234”
  Default speed is 115200 bps (8-N-1)
Bluetooth

## Slide 10: All the Pieces
Teensy 3.6
Microphone
Aux Input
Microphone
Bluetooth
Teensy Audio Board
System
Power
Built-In Mics
Vs Aux Input
Bias for
Aux Input
Battery
Headphone
Jack
User Knob (Gain)
USB for Power
and Programming

## Slide 11: Reprogramming
This device is built around the Teensy 3.6, which is aimed at hobbyists
It is programmed like an Arduino.
  If you’ve never worked with an Arduino, you should start with an Arduino. See my guide here.
Once you get the Arduino stuff running, install the Teensy extensions
  See my guide here [not yet ready…see here instead]
Finally, you can download my hearing aid examples
  See my guide here [not yet ready]
    My blog shows me working with the hardware here.
    My library for Arduino/Teensy in my GitHub repo here
    More programs are at my other other GitHub repo here.