## Slide 1: Tympan – Prototype A

## Slide 2: Hardware Elements
Line-In / Mic Jack
Headphone Jack
USB to
Program/Recharge
On-Board Mic
Power
Switch
User Pot
(Volume)
Bluetooth
Classic
On-Board Mic
User
LEDs
Li-Po Battery on Back

## Slide 3: Variety of Inputs
Use On-Board Microphones
Use External Microphone2
Two On-Board MEMS Microphones:
Knowles SPH1642
Stereo Jack for Mics or Line-In.
Software-Selectable Bias Voltage.

## Slide 4: Battery-Powered to Be Wearable

## Slide 5: Hardware Specs
Processor
  NXP MK66F (ARM Cortex M4F Core)
  180 MHz with Floating-Point Unit
Analog-Digital
  Texas Instruments TLV320AIC3106, stereo ADC and DAC
  32/24/20/16-bit configurable (93 dB SNR)
  Low-noise, software-controllable gain on inputs
  Software-controllable microphone bias
  Software-controllable headphone amplifier
Data Interfaces
  USB Serial, USB Audio, USB HID
  Bluetooth Classic
  SD Card
  Digital microphone port
Power
  Draws about 100 mA @ 3.7V.
  Power from USB or Li-Po Battery
  On-board recharging from USB (with indicators)
Programming
  Reprogram via USB. Program in C/C++.
  Free, open-source toolchain
User Interaction
  Potentiometer, LEDs, Bluetooth